## Slide 1: Chemical Monitoring, Part B
Learning Module #6

## Slide 2: Agenda
Time | Length | Activity
1:00 | 10 min | Opening Activity
1:10 | 1 hour | Adopt-A-Stream protocols for Chemical Monitoring
2:10 | 20 min | Compare and Contrast
2:30 | 15 Min | BREAK
2:45 | 1 hour, 25 min | Chemical Monitoring in our Campus Stream
4:10 | 15 Min | Closing Activity

## Slide 3: Opening Activity
Instructions:
Write your response to the questions on the paper.
Share with a partner
Class discussion

## Slide 4: Opening Activity
Have you ever measured water temperature or pH before? If so, how did you do each?

## Slide 5: Protocols for Chemical Monitoring
You will need:
Field directions for Chemical Monitoring
Chemical Monitoring Form
Pencil/Clipboard
Gloves
Safety Glasses
Sample water
Waste Jug
Conductivity/Temperature Probe
pH sampling Kit
Dissolved Oxygen Sampling Kit
Make sure to wear GLOVES and SAFTEY GLASSES at all times when handling chemicals!

## Slide 6: 1) Temperature/Conductivity
Measured with one probe!
Image: Fisher Scientific

## Slide 7: 1a) Temperature
Notes:
 Record air temperature before water temperature
 Take one measurement for air temperature and water temperature
Directions:
1. Air temperature - place the dry thermometer in a shady area and record temperature after reading stabilizes. Record temperature in degrees Celsius to the nearest 0.5 degree.
2. Water temperature - take the temperature reading of the water in the shade. It is best to take the temperature reading directly in the stream, but if you cannot, place thermometer directly into a bucket of sample water (in the shade) and record temperature. Take reading after temperature has stabilized (about 2 minutes). Record temperature in degrees Celsius to the nearest 0.5 degree.

## Slide 8: Discussion question:
Why do you think measure air temperature before water temperature?

## Slide 9: 1b) Conductivity
Notes:
Take one measurement for this parameter
PROBES HAVE ALREADY BEEN CALIBRATED!!
Directions:
Remove electrode cap. Turn the meter on (On/Off Key).
Dip electrode into waterbody. Make sure sensor is fully covered.
Wait for reading to stabilize (Automatic Temperature Compensation corrects for temperature changes).
Press ‘Hold’ and record reading on data sheet.

## Slide 10: Discussion question:
Why do you think we need to calibrate conductivity probe?

## Slide 11: 2) pH
Notes:
Take two measurements, the duplicate precision rule for pH is 0.25 standard units
Hold reagent bottle vertical to ensure uniform drops
Use a white background and view the comparator box with the light shining over your shoulders into the comparator.
Directions:
1. Rinse two small glass tubes twice with sample water.
2. Fill each tube to the 5 mL line with sample water. If using the octa-slide 2 viewer pH test, fill each tube to the 10 mL line and proceed with next step. Overfill the tube and ‘flick’ out excess water. Ensure that the meniscus is at the fill line.
3. Add 10 drops of the pH wide range indicator to each tube.
4. Cap and gently invert the tubes several times to ensure mixing.
5. Use the color comparator boxes to determine the pH level.
6. Record pH to the nearest 0.25 standard units. **Pour sample into waste jug
7. Rinse glass vials and caps with distilled water so they are ready for your next sampling event. **Pour any sample waste into waste jug

## Slide 12: Discussion question:
Why do you think we are instructed to take pH measurements twice (instead of once)?

## Slide 13: 3) Dissolved Oxygen
Notes:
Take two measurements for dissolved oxygen, the duplicate precision rule for dissolved oxygen is +/- 0.6 mg/L
Hold reagent bottles vertical to ensure uniform drops
A- Collect two replicate samples to ensure precision
1. Using the two dissolved oxygen sample bottles in your kit, remove caps and rinse bottles twice with stream water. In a well-mixed area of the stream, hold both bottles under water and carefully fill them completely with water, avoiding trapping air bubbles or bubbling air into the sample (which may add dissolved oxygen) and cap under water. Avoid collecting samples in areas that you have disturbed the substrate.

## Slide 14: 3) Dissolved Oxygen
B- “Fixing” the samples
Note: “fix” both sample bottles at the same time
2. In quick succession, add 8 drops of Manganous Sulfate Solution to each sample bottle then 8 drops of Alkaline Potassium Iodide Azide to each sample bottle. Cap the bottles and invert several times. Wait until the precipitate settles below the shoulder of the bottle before proceeding to step 3.
3. Add 8 drops of Sulfuric Acid 1:1. Cap and repeatedly invert bottles until the brown flakes dissolve. This may take some time, so be patient. Once this step is complete, the solution is now “fixed” and may range in color from yellow to orange brown

## Slide 15: 3) Dissolved Oxygen
C- Titrating the sample
Note: Process one sample bottle at a time
4. Rinse the titration tube twice with a small amount of the fixed sample. Dispose of rinse water in the waste jug. Next, place 20 mL of the fixed sample into the glass titration vial for analysis.
5. Using the pink tip, fill the titrator (small syringe) to the 10mL line with Sodium Thiosulfate. Make sure no bubbles are in the titrator. Place the titrator into the hole in the cap of the glass titration vial, or, depending on which kit is used, hold the eyedropper above the fixed sample.
6. Slowly add Sodium Thiosulfate from the titrator into the sample. After each drop, swirl to thoroughly to mix the Sodium Thiosulfate throughout the solution. Continue one drop at a time until the solution turns a pale straw yellow color. *Note-High light intensity degrades Sodium Thiosulfate - do not allow the sample bottle to be exposed to the sun for long periods of time.
7. Remove the titration vial cap and titrator CAREFULLY so as not to lose any of the Sodium Thiosulfate (you will continue titrating in step 9). Add 8 drops of Starch Solution to the titration vial that is holding the sample. The sample will turn dark blue. Continue titrating with Sodium Thiosulfate ONE DROP AT A TIME, swirling thoroughly after each drop, until the solution turns from blue to clear.
8. Read the amount of dissolved oxygen in your sample directly from the syringe (direct reading titrator). Tick marks measure 0.2 ppm. Read the final dissolved oxygen value at the liquid side of the green plunger disk inside the titrator.
9. Repeat the procedures of Step C for the second sample bottle.

## Slide 16: Discussion question:
Why do you think we need to ensure that there is no air in the DO sample bottle?

## Slide 17: YSI Probe
Image: Cole-Parmer

## Slide 18: Compare and Contrast – YSI Probe and Adopt-A-Stream Protocols
Image: Cole-Parmer

## Slide 19
 | Adopt-A-Stream Protocols | YSI Probe
Pros |  | 
Cons |  | 

## Slide 20
Take
a
break!

## Slide 21: Chemical Monitoring of our Campus Stream
SAFETY
FIRST

## Slide 22: Chemical Monitoring of our Campus Stream
You will need:
Field directions for Chemical Monitoring
Chemical Monitoring Form
Pencil/Clipboard
Gloves
Safety Glasses
Waste Jug (one per class)
Conductivity/Temperature Probe (one per group)
pH sampling Kit (one per group)
Dissolved Oxygen Sampling Kit (one per group)
Water boots
Backpack
Make sure to wear GLOVES and SAFTEY GLASSES at all times when handling chemicals!

## Slide 23: Closing Activity
Instructions:
Write your response to the questions on the lesson worksheet.

## Slide 24: Closing Activity
Question 1: You are a water researcher for Athens Clarke County. You are going to be in charge of an upcoming water quality sampling event of the North Oconee River, and will take place four times per year. The sampling event will including measuring temperature, conductivity, dissolved oxygen, and pH. You are sponsored by a large corporation that has given you a $10,000 budget for the sampling. Would you choose to use Georgia Adopt-a-Stream protocols for chemical monitoring, or a YSI probe? Explain your answer.
Question 2: Why do we measure pH twice using Georgia Adopt-A-Stream protocols?