## Slide 1: Data Accuracy
Learning Module #9

## Slide 2: Agenda
Time | Length | Activity
9:00 | 25 min | Video – Clean Water Act and TMDLs
9:25 | 55 min | Procedure comparison
10:20 | 15 min | Analytical Labs
10:35 | 15 min | BREAK
10:50 | 1 hour, 30 min | Field trip to Analytical Lab
12:20 | 10 min | Closing Activity

## Slide 3: Video – Clean Water Act and TMDLs
Let’s learn about the Clean Water Act and TMDLs by watching this video:
https://lawshelf.com/shortvideoscontentview/the-clean-water-act/

## Slide 4: Video – Clean Water Act and TMDLs
Now, work with a partner to answer questions from the video on your lesson worksheet.
You may use the transcript of the video and your memory of the video to help you answer the questions!

## Slide 5: Video – Clean Water Act and TMDLs: Discussion
What is the purpose of the Clean Water Act?
Does the Clean Water Act regulate point source or non-point source pollution?
What is one example punishment for violating the Clean Water Act?
What does it mean for a water body to be “impaired”?
What is a TMDL (in other words, a Total Maximum Daily Load)?
What kind or kinds of water is not included in the Clean Water Act?

## Slide 6: Video – Clean Water Act and TMDLs: Discussion
Do you think punishments for violating the Clean Water Act are fair? Why or why not?
Why is it important to accurately measure the amount or concentrations of pollutants in a water body?

## Slide 7: Procedure comparison
We have learned that there is usually more than one way/method/procedure to measure a water quality parameter (nutrients, dissolved oxygen, pH, etc.).
Today, we are going to compare for nitrate and phosphorus concentrations measured by two different procedures – the Hach Colorimeter (Adopt-A-Stream methods; non-professional) and by an Analytical Laboratory (a professional laboratory).

## Slide 8: How do we compare measurements from two procedures?

## Slide 9: How do we compare measurements from two procedures?
There are multiple ways to compare measurements from two procedures

## Slide 10: How do we compare measurements from two procedures?
There are multiple ways to compare measurements from two procedures
One simple way to compare measurements from two different procedures is to plot the results in a scatter plot, add a trendline, and determine the R2 value.

## Slide 11: How do we compare measurements from two procedures?
There are multiple ways to compare measurements from two procedures
One simple way to compare measurements from two different procedures is to plot the results in a scatter plot, add a trendline, and determine the R2 value.
R2 – a statistical measure that indicates how much variation of the dependent variable (y-axis) is explained by the independent variable (x-axis).

## Slide 12: Let’s look at an example!
pH - Procedure A
pH - Procedure B

## Slide 13: Let’s look at an example!
pH - Procedure A
pH - Procedure B
Line of best fit – line through scatter plot that best expresses the relationship between the points

## Slide 14: Let’s look at an example!
pH - Procedure A
pH - Procedure B
Line of best fit – line through scatter plot that best expresses the relationship between the points
R2 = 100%

## Slide 15: Let’s look at an example!
pH - Procedure A
pH - Procedure B
Line of best fit – line through scatter plot that best expresses the relationship between the points
R2 = 100%
This means that 100% of the variation in the y axis (Procedure B results) can be explained by the results from Procedure A.

## Slide 16
pH - Procedure A
pH - Procedure B
R2 = 100%
pH - Procedure A
pH - Procedure B
R2 = 80%
pH - Procedure A
pH - Procedure B
R2 = 40%
pH - Procedure A
pH - Procedure B
R2 = 0%

## Slide 17
pH - Procedure A
pH - Procedure B
R2 = 100%
pH - Procedure A
pH - Procedure B
R2 = 80%
pH - Procedure A
pH - Procedure B
R2 = 40%
pH - Procedure A
pH - Procedure B
R2 = 0%

## Slide 18
pH - Procedure A
pH - Procedure B
R2 = 100%
pH - Procedure A
pH - Procedure B
R2 = 80%
pH - Procedure A
pH - Procedure B
R2 = 40%
pH - Procedure A
pH - Procedure B
R2 = 0%

## Slide 19
pH - Procedure A
pH - Procedure B
R2 = 100%
pH - Procedure A
pH - Procedure B
R2 = 80%
pH - Procedure A
pH - Procedure B
R2 = 40%
pH - Procedure A
pH - Procedure B
R2 = 0%

## Slide 20: Now, let’s practice!
Open the Excel file that the instructor sent you.
We will run through 1-2 examples together of how to:
  Graph a scatter plot
  Add a trendline
  Add the R2 value
You will then create your own graphs comparing nitrate and phosphorus concentrations from the Hach Colorimeter (non-professional) and the Analytical Lab (professional lab).
Create the graph son your Excel sheet, but answer the associated questions on your worksheet.

## Slide 21: Graphing activity!
Once you have completed graphs on Sheet 3 (Nitrate) and Sheet 4 (phosphorus), don’t forget to answer the final questions on your lesson worksheet.

## Slide 22: Final Questions for Graphing Activity
In your own words, how did the Hach Colorimeter measurements compare to the Analytical Lab measurements for nitrate? What about for phosphorus?
If you owned a paper mill and the stream by your factor was being tested for water quality, would you want the EPA to use the Hach Colorimeter test or the Analytical Lab to test for nutrient concentrations? Why?

## Slide 23: What is an analytical laboratory?
Analytical laboratories offer professional services that classify, assay and/or analyze chemical, material, biological, geological and environmental samples.
Photo credit:
Photographer Daniel SoneNational Cancer Institute,
Public domain, via Wikimedia Commons

## Slide 24: What kinds of samples to analytical laboratories analyze?
/www.globalspec.com
Notes: Bioanalytical (Assays, Drug Discovery): Bioanalytical laboratories perform agricultural, biological, microbial, pharmaceutical and other life sciences testing and analysis services. As part of the larger field of biotechnology, these laboratories provide services throughout the drug development cycle, performing pharmacokinetic and pharmacodynamic screening and provide expertise with mammalian cell-based assays, biomarkers, radiochemistry, immunoassays, and electrophoresis.
Food and Beverage Testing: These laboratories perform tests to ensure that food and beverages are safe for human and animal consumption. They can also provide nutritional analyses including vitamins and sugars.
Cleanliness Monitoring/Testing: Cleanliness monitoring test samples from air, surfaces, and labware of a manufacturing, processing, or laboratory facility for contamination
Environmental Testing and Analysis Services: These laboratories provide testing of environmental samples such as soil, water, air, and industrial wastes or byproducts.
Failure Analysis: Failure Analysis testing determines how and why materials or components fail.
Industrial Hygiene Services: Laboratories offering industrial hygiene services test samples from workplaces and calculate potential exposure to hazardous substances.
Stack Emissions/Opacity Testing: Stack testing services take samples from a single sampling location in a facility and test for pollutant emission rates, concentration or other parameter. Opacity testing measures smoke emitted from gas- or diesel-fired vehicles.
Water Quality Monitoring /Audit Services: These services provide ongoing testing for ground water and surface water, for contaminants including organic and inorganic compounds, heavy metals, PCBs, and biological organisms.
Standards Testing/Certification: Standards testing services verify that materials meet established standards by organizations such as the American Society for Testing and Materials (ASTM).
Toxicity/ Reactivity Testing: Toxicity/ reactivity analysis is used to determine the toxicity, reactivity, corrosivity, ignitability, or flammability of a substance.

## Slide 25: What kinds of samples to analytical laboratories analyze?
Bioanalytical (Assays, Drug Discovery)
Food and Beverage Testing
Cleanliness Monitoring/Testing
Environmental Testing and Analysis Services
Failure Analysis
Industrial Hygiene Services
Stack Emissions/Opacity Testing
Water Quality Monitoring Standards Testing/Certification
Toxicity/ Reactivity Testing
/www.globalspec.com
Notes: Bioanalytical (Assays, Drug Discovery): Bioanalytical laboratories perform agricultural, biological, microbial, pharmaceutical and other life sciences testing and analysis services. As part of the larger field of biotechnology, these laboratories provide services throughout the drug development cycle, performing pharmacokinetic and pharmacodynamic screening and provide expertise with mammalian cell-based assays, biomarkers, radiochemistry, immunoassays, and electrophoresis.
Food and Beverage Testing: These laboratories perform tests to ensure that food and beverages are safe for human and animal consumption. They can also provide nutritional analyses including vitamins and sugars.
Cleanliness Monitoring/Testing: Cleanliness monitoring test samples from air, surfaces, and labware of a manufacturing, processing, or laboratory facility for contamination
Environmental Testing and Analysis Services: These laboratories provide testing of environmental samples such as soil, water, air, and industrial wastes or byproducts.
Failure Analysis: Failure Analysis testing determines how and why materials or components fail.
Industrial Hygiene Services: Laboratories offering industrial hygiene services test samples from workplaces and calculate potential exposure to hazardous substances.
Stack Emissions/Opacity Testing: Stack testing services take samples from a single sampling location in a facility and test for pollutant emission rates, concentration or other parameter. Opacity testing measures smoke emitted from gas- or diesel-fired vehicles.
Water Quality Monitoring /Audit Services: These services provide ongoing testing for ground water and surface water, for contaminants including organic and inorganic compounds, heavy metals, PCBs, and biological organisms.
Standards Testing/Certification: Standards testing services verify that materials meet established standards by organizations such as the American Society for Testing and Materials (ASTM).
Toxicity/ Reactivity Testing: Toxicity/ reactivity analysis is used to determine the toxicity, reactivity, corrosivity, ignitability, or flammability of a substance.

## Slide 26: What kinds of samples to analytical laboratories analyze?
Bioanalytical (Assays, Drug Discovery)
Food and Beverage Testing
Cleanliness Monitoring/Testing
Environmental Testing and Analysis Services
Failure Analysis
Industrial Hygiene Services
Stack Emissions/Opacity Testing
Water Quality Monitoring Standards Testing/Certification
Toxicity/ Reactivity Testing
/www.globalspec.com
Notes: Bioanalytical (Assays, Drug Discovery): Bioanalytical laboratories perform agricultural, biological, microbial, pharmaceutical and other life sciences testing and analysis services. As part of the larger field of biotechnology, these laboratories provide services throughout the drug development cycle, performing pharmacokinetic and pharmacodynamic screening and provide expertise with mammalian cell-based assays, biomarkers, radiochemistry, immunoassays, and electrophoresis.
Food and Beverage Testing: These laboratories perform tests to ensure that food and beverages are safe for human and animal consumption. They can also provide nutritional analyses including vitamins and sugars.
Cleanliness Monitoring/Testing: Cleanliness monitoring test samples from air, surfaces, and labware of a manufacturing, processing, or laboratory facility for contamination
Environmental Testing and Analysis Services: These laboratories provide testing of environmental samples such as soil, water, air, and industrial wastes or byproducts.
Failure Analysis: Failure Analysis testing determines how and why materials or components fail.
Industrial Hygiene Services: Laboratories offering industrial hygiene services test samples from workplaces and calculate potential exposure to hazardous substances.
Stack Emissions/Opacity Testing: Stack testing services take samples from a single sampling location in a facility and test for pollutant emission rates, concentration or other parameter. Opacity testing measures smoke emitted from gas- or diesel-fired vehicles.
Water Quality Monitoring /Audit Services: These services provide ongoing testing for ground water and surface water, for contaminants including organic and inorganic compounds, heavy metals, PCBs, and biological organisms.
Standards Testing/Certification: Standards testing services verify that materials meet established standards by organizations such as the American Society for Testing and Materials (ASTM).
Toxicity/ Reactivity Testing: Toxicity/ reactivity analysis is used to determine the toxicity, reactivity, corrosivity, ignitability, or flammability of a substance.

## Slide 27: Why are analytical laboratories important?

## Slide 28: Why are analytical laboratories important?
Many different people, scientists, and companies require accurate measurements of substances to ensure samples (food, drug, water, environmental etc.) meet certain standards.

## Slide 29: Why are analytical laboratories important?
Accuracy: how close the measurements are to the truth
Precision: how close the measurements are to each other
High accuracy
High precision
Low accuracy
Low precision
Low accuracy
High precision
High accuracy
Low precision

## Slide 30: Why are analytical laboratories important?
Many different people, scientists, and companies require accurate measurements of substances to ensure samples (food, drug, water, environmental etc.) meet certain standards.
Testing equipment is often very expensive. Sometimes, it makes sense for scientists to “send off” samples to a laboratory, rather than try to conduct the analyses on their own.

## Slide 31
Take
a
break!

## Slide 32: Field trip to Analytical Laboratory!

## Slide 33: Closing Activity
Instructions:
Write your response to the question on your lesson worksheet.

## Slide 34: Closing Activity
Question 1: In your own words, why is taking accurate measurements of water pollution (like nutrient concentrations) important?